Product Guarantee

Plast-O-Matic guarantees its products to be free from defects in material or workmanship over a period of one (1) year from date of shipment from its factory.

If any product is found unsatisfactory under this Guarantee, the purchaser should notify Plast-O-Matic in writing or phone, and after receipt of Plast-O-Matic’s shipping approval, the purchaser may return it directly to Plast-O-Matic’s factory in New Jersey (USA), shipping charges prepaid.

Such products will be inspected by Plast-O-Matic and if determined defective due to material or workmanship shall be replaced or put in proper operating condition, free of all charges, including ground freight, and a credit will be allowed for ground freight to Plast-O-Matic. The correction of any defects by repair or replacement by Plast-O-Matic shall constitute fulfillment of all obligations and liability of Plast-O-Matic to the purchaser under this Guarantee.

Plast-O-Matic is not responsible for damage to its products through improper installation, maintenance, use or attempts to operate it beyond its mechanical or electrical capacity intentionally or otherwise, or for unauthorized repair including freight charges.

Any failure to notify Plast-O-Matic immediately of unsatisfactory operation, or any improper or unauthorized installation, maintenance, use, repair or adjustments, shall terminate this Guarantee and shall relieve Plast-O-Matic from any further responsibility thereunder.

Plast-O-Matic shall not be liable for special or consequential damages in any claim, action, suit, or proceedings arising under this Guarantee, nor shall there be any liability thereunder for claims for labor, loss or profit or good will, repairs or other expenses incidental  to replacement.

The foregoing warranty is exclusive and in lieu of any and all other warranties, expressed or implied. No warranty of merchantability, no implied warranty of fitness for any particular purpose, and no implied warranty arising by usage of trade, course of dealing or course of performance is given by seller or shall arise by or in connection with this sale and/or the seller’s and/or buyer’s conduct in relation thereto or to each other, and in no event shall seller be liable on any such warranty with respect to any product.

PLAST-O-MATIC VALVES, INC.

1384 Pompton Avenue

Cedar Grove, NJ 07009-1095

( Telephone	(973) 256-3000

( Fax 		(973) 256-4745

( e-mail  info@plastomatic.com

i&mckd.doc  Rev. 1-Apr-99

INSTALLATION & MAINTENANCE INSTRUCTIONS

IMPORTANT - BEFORE INSTALLING

CKD check valves will prevent back flow when properly installed and used within the recommended ranges of pressure, temperature, and chemical compatibility.  The ultimate determination of material compatibility is previous successful use in the same application.  Call our Technical Support for information about your application.

Caution: Plastic materials will degrade in ultraviolet (UV) light or sunlight.

Caution: Polypropylene and PVDF (Kynar) often look similar. Do not install in your system if you are not sure.

MAXIMUM INLET PRESSURES for WATER*

BODY MAT’L

COLOR

77 oF

| (25 oC) | 105 oF (40 oC) |
| --- | --- |

at MAXIMUM

TEMPERATURE

PVC

DARK GRAY

140 PSI

10 Bar

100 PSI

7 Bar

40 PSI @ 140 oF

| 3 Bar @ 60 oC |
| --- |
| Polypro | TRANSLUCENT WHITE |

125 PSI

7 Bar

100 PSI

7 Bar

25 PSI @ 180 oF

2 Bar @ 105 oC

Kynar

| PVDF | TRANSLUCENT WHITE (yellowish) |
| --- | --- |

100 PSI

10 Bar

100 PSI

8 Bar

30 PSI @ 280 oF

2 Bar @ 140 oC

Teflon

PTFE

OPAQUE WHITE

100 PSI

3 Bar

80 PSI

2 Bar

5 PSI @ 300 oF

35 KPa @ 140 oC

*or compatible chemical - ratings reduced for some applications.

Minimum temperature 40oF (5oC).

EPDM seals limited to 250 oF (120oC), Buna-N to 200 oF (95oC).

KYNAR is a trademark of Elf Atochem

TEFLON is a trademark of Dupont Company

See the Product Data Sheet or consult our Technical Support staff for more information.

INSTALLATION INSTRUCTIONS

The valve must be installed in the proper flow direction as indicated by the flow label.  Because the disc and diaphragm will sink in water, the flow direction should point up. This way the valve will seal even in low flow conditions.

Caution: For liquids heavier than water, where the disc and diaphragm float in the process liquid, the flow direction should point down so that the diaphragm floats against the seal.

THREADED CONNECTION - A suitable thread sealant (ex. Teflon® tape) should be applied to male tapered threads to assure a “leak-tight” seal. The assembly need only be made “hand-tight” followed by a quarter (1/4) turn with a strap wrench.  Do not over tighten or use pipe wrenches on plastic pipe and components.

Caution: Teflon® tape will “string” as pipe threads are joined.  Loose “strings” could lay across the seating surface and prevent the valve from completely closing.  To avoid this problem, clean out old tape, and do not apply tape to the first thread.

Caution: Connections should be made only to plastic fittings; metal pipe should only be installed with an intervening plastic nipple.  Metal pipe and straight threaded pipe tend to cut, stretch, and distort the plastic bodies, which could result in cracking or leaking over time.

NON-THREADED CONNECTIONS - For solvent cementing or heat fusion, follow instructions supplied with the cement or fusion equipment, or contact your distributor.

MAINTENANCE

Plast-O-Matic recommends keeping a spare seal kit available for repairs.  Seal life will vary in applications due to cycles, temperatures, pressures, chemicals, and concentration. Based on the application, a periodic inspection and maintenance plan should be established.  The seal kit part number is “SK” plus the part number less the material suffix.  For example, the seal kit for CKD050V-PV is SKCKD050V.  The seal kit contains one O-ring and one diaphragm.

PARTS & ILLUSTRATION

| # | QTY | DESCRIPTION | MATERIAL |
| --- | --- | --- | --- |
| 1 | 1 | INLET SIDE | see note 2 |
| 2 | 1 | DIAPHRAGM | see note 1 |
| 3 | 1 | LOOSE DISC | see note 2 |
| 4 | 1 | O-RING | see note 1 |
| 5 | 1 | OUTLET SIDE | see note 2 |

( Seal elastomer suffix:  EP for EPDM,  V for Viton(

( Material suffix:   PV  for PVC,   PP for Polypropylene,  TF for PTFE, PF for PVDF.

VITON is a registered trademark of the DuPont Company

# Text boxes

DIAPHRAGM CHECK VALVES

Series CKD